## Slide 1
Photo: 7/24/2012
Maclure Cr. Gage:
updated 6/24/2015
Photo: 6/24/2015
Elevation: 10,020 ft
Lat: 37.7722 Long: -119.2644 Datum: WGS84

## Slide 2
Maclure
Creek
Lyell Fk. below
Maclure Cr
JMT/PCT

## Slide 3
New LOW WATER TD bolt, TDB1
installed 6/24/2015
*measure from X on bolt*
Old TD rebar, used as datum from 2012-2014 for WWQ
Vented P.T. mount,
CS 450 installed
6/15/2014,
(hard to see)
Photo: 6/24/2015
FLOW

## Slide 4
New HIGH WATER TD BOLT
TDB2, measure down to X. Gage height of
TDB2 top = 10.273
BM1, between enclosure tree and TD B2
6/24/2015 Level survey notes:
Photo: 6/24/2015
Location | Benchmark manufacturer #s on stainless bolt heads | Actual Survey Rod measurements (ft.) | Relative Elevations (ft.) with making BM1=100' | Distance from BM1(ft.) | Azimuth from BM1(deg) | Notes
TDB1 Middle of X | F593C w/ X cut for TD measurements | 7.335+0.02=7.355 | 97.182 | 30.26 | 125 | TB1 is colocated w/ old rebar TD and can be used for low flows (on opposite side of river)
Old TD Rebar Top | NA | 7.235 | 97.302 | 30.22 | 125 | 
TDB2 Top | 316 TH | 7.082 | 97.455 | 10.75 | 154 | TB2 is on river left and is oriented so that in high flows it can be measured under water.
BM1 Top | Bolt with cut X mark. | 4.537 | 100 | NA | NA | BM1 is on river left, between enclosure-tree and TDB2

## Slide 5
Photo: 6/23/2015
Station Inventory: 6/24/2015
Datalogger: CR1000 SN:11803
CS451-L Pressure Transducer 50’ cable, SN: 20010323
CS547 Spec Conductance 30’ cable, Kc: 1.38, SN: 6182
CH100 Charge controller 12V SN: 6668
12 Ah. Internal battery, 12V, Model: NP12-12T
20 Watt Extreme Power Corp Solar Panel
Data logger program stored under 6/24/2015 field visit
hydrometric notes In Aquarius .
Photo: 6/24/2015

## Slide 6
Photo: 6/23/2015

## Slide 7
Photo: 7/24/2012
Photo: 8/21/2013